## Slide 1: DESCRAMBLE
Executive Summary
Project description:
The “Drilling in dEep, Super-CRitical AMBient of continentaL Europe” (DESCRAMBLE) project proposes to drill in continental-crust, super-critical geothermal conditions, and to test and demonstrate novel drilling techniques to control gas emissions, the aggressive environment and the high temperature/pressure expected from the deep fluids. The project will improve knowledge of deep chemical-physical conditions for predicting and controlling critical drilling conditions. An existing well in Larderello (Tuscany, Italy), Venelle_2, will be deepened from its present depth of 2.2 km down to 3-3.5 km. The DESCRAMBLE project will be partly supported by EU H20202 funds: cost 15,2 M€, grant 6,7 M€. The final purpose of the project is the chemical and thermo-physical characterization of the steam reservoir. The Venelle_2 well will not be converted in a production well.

## Slide 2: DESCRAMBLE
Executive Summary
PHASE I DESCRAMBLE: DEEPENING VENELLE_2 WELL
PHASE II PILOT PLANT
PHASE III FULL DEPLOYMENT
  The DESCRAMBLE PROJECT is the first part of an innovation path in three phases:
  • PHASE I – R&D: the activity partly financed by H2020 of deepening the Venelle_2 well, for testing new material and procedure for drilling and fluid handling in supercritical conditions (450°C and 250 bar). The probability of success of this phase is about 30%;
  • PHASE II - PILOT: in case of success of PHASE I, a Pilot Plant of 40 MW could be realized, fed by a two supercritical wells, with possibility of grants from EU (as follow up of DESCRAMBLE), MIUR and Tuscan Region; the probability of success of this phase is about 80%.
  • PHASE III - Deployment: after the R&D and Pilot phases, the supercritical plant could be replied in different locations in Italy and abroad, with a substantial cost reduction due to a learning curve effect.
  Under evaluation by Investment Committees
  Future Developments of the Project

## Slide 3: DESCRAMBLE
Work Breakdown Structure and Partners

## Slide 4: DESCRAMBLE
Innovative Aspects
HIGHLIGTH ON THE MOST INNOVATIVE ASPECTS
Applied research/demonstrations of industrial component in an unconventional application:
Materials: Bottom hole assembly components, Cementing process, Drilling fluids, Well materials (casing, well head, and cement
Well design and control: the research will optimize new procedures, explicitly utilizing synergies with oil and gas industry.
Predicting and controlling super-critical conditions: the research will optimize new procedures, explicitly using synergies with oil and gas industry. Existing simulators will be extended to the super-critical regime.
Development of a new logging tool: suitable for measurement of pressure and temperature at supercritical conditions.
Scientific research aspects: Seismic characterization of the super critical region, Petrophysics and log interpretation, Geochemical monitoring and Petrology

## Slide 5: DESCRAMBLE
Benefits
HIGHLIGTH ON THE MOST IMPORTANT BENEFITS
Increased power output per well (5-10 fold)
Production of a higher value steam (higher P-T)
Extending the resource base and lifetime of existing fields
Knowledge of reservoir characteristics at greater depths
Advancing techniques of UGR (Unconventional Geothermal Resources)
Development of an environmentally benign resource
Development of high-temp. instruments and drilling technology
Application to high-temp. geothermal systems world wide
Educational, industrial and economic spin offs